## Slide 1
ASSAM · JAL JEEVAN MISSION · CSAT AI
Phase 1
Beneficiary
Satisfaction
Results
45,863
Calls
2,373
Schemes
35
Districts
7
Zones
2.20
out of 5.0
STATE BSI SCORE
Beneficiary Satisfaction Index
🟡 MODERATE — 42.8% of max
Target ≥ 3.5 / 5.0
April 2026 · AI Voice-Bot Survey · Confidential

## Slide 2
PROGRAMME OVERVIEW
What was done and why
📋 What is this?
AI voice-bot survey across all JJM water supply schemes in Assam
45,863 households called over Phase 1
Beneficiaries asked 5 questions about their tap water supply
No human interviewer — automated outbound IVR calls
🎯 Why are we doing it?
2,373 JJM schemes — manual surveys are impossible at this scale
Government needs scheme-level satisfaction data to act on
AI bot enables cost-effective, consistent, repeat-cycle surveying
Phase 1 establishes the baseline BSI for future comparison
📊 What does BSI measure?
BSI = Beneficiary Satisfaction Index — score out of 5.0
5 weighted questions: Quality, Quantity, Daily supply, Timing, Overall
Aggregated: Household → Scheme → District → Zone → State
≥3.5 = Good · 2.0–3.5 = Moderate · <2.0 = Critical

## Slide 3
CALL FUNNEL
Where did 45,863 calls go?
Follow the funnel top to bottom — each step shows how many people remained engaged.
STEP 1 — Bot dials household
All call attempts in Phase 1
45,863
100%
100% of total
STEP 2 — Person consents
27.4% agreed | 69.1% hung up immediately
12,583
27.4%
27.4% of total
STEP 3 — Answers Q1 (usable)
Only these calls contribute to any scoring
9,224
20.1%
20.1% of total
STEP 4 — Completes full survey
Answered all 5 questions
1,578
3.4%
3.4% of total
⚠ 19,909 calls (43.4%) ended under 30 seconds — zero data. Single biggest fix: redesign the opening bot script.

## Slide 4
KPI SATISFACTION RESULTS
% of respondents satisfied per survey question
5 questions asked. Scores below show the % who answered 'Yes / Satisfied'.
Q2
Water Quality
"Is the water clean enough?"
72.3%
Strongest KPI — best performing dimension
70% target
Q3
Water Quantity
"Is there enough water?"
62.2%
Moderate — gaps in BTAD and Barak Valley
Q4
Consistent Timing
"Does it arrive at a fixed time?"
57%
Operations issue — not infrastructure
Q5
Overall Satisfied
"Are you satisfied with your supply?"
52.2%
25.2% actively dissatisfied
Q1
Water Daily
"Did water come every day (7 days)?"
31%
WEAKEST — 69% report days without water
Overall split:
52.2% Satisfied
22.6% Neutral
25.2% Dissatisfied

## Slide 5
ZONE-LEVEL PERFORMANCE
BSI score per zone | 0.70+ = Good · No zone currently meets this benchmark
Zone
BSI Score /1.0
Calls Made
Valid Schemes
Assessment
North Assam
0.484
12,830
252
Highest BSI — most responsive
Upper Assam
0.479
8,302
174
Strong — Upper Assam performing well
KAAC
0.463
1,095
13
Above average — limited sample
Lower Assam
0.455
12,995
173
Close to state average
Barak Valley
0.379
8,603
48
Low — Bengali region, wrong language bot
BTAD
0.384
1,943
17
Critical — infrastructure failures
DHAC
N/A
95
—
No data — 95 calls, 1.1% consent
State total: 0.4406 / 1.0 (44.1%) · Benchmark ≥ 0.70 = Good · No zone meets this benchmark in Phase 1

## Slide 6
DISTRICT PERFORMANCE
Top 5 and bottom 5 districts by BSI score · 35 districts total
🏆 Top 5 Districts — highest BSI
Sivasagar
Upper Assam
0.532
Top 1
Dhubri
Lower Assam
0.521
Top 2
Jorhat
Upper Assam
0.527
Top 3
Golaghat
Upper Assam
0.517
Top 4
Bajali
Lower Assam
0.487
Top 5
⚠ Bottom 5 Districts — priority intervention
Hailakandi
Barak Valley
0.279
Critical
Tamulpur
BTAD
0.329
Critical
Baksa
BTAD
0.355
Critical
Chirang
BTAD
0.400
Needs Attention
Udalguri
BTAD
0.371
Needs Attention
Score gap: Best district (Sivasagar 0.532) vs Worst (Hailakandi 0.279) = 1.9× · State average of 0.44 masks enormous local variation

## Slide 7
SCHEME COVERAGE & PERFORMANCE BANDS
2,373 schemes total · How many have enough data?
🏗 Scheme Coverage — 2,373 total
✅ Valid — ≥ 6 usable responses
615
25.9%
Statistically valid. Used in all scoring.
⚠ Flagged — 1 to 5 responses
1,426
60.1%
Scored but excluded from aggregations.
❌ No data — 0 responses
~332
14.0%
Bot did not reach — re-call in Phase 2.
17.6%
Functional
82.4%
Non-Functional
📊 Performance Bands — schemes per dimension
Regularity
497
1305
332
55% critical
Timeliness
512
402
1232
52% critical
Quantity
722
525
443
683
30% critical
Quality
1002
375
293
703
42% critical
Overall Sat
549
438
643
743
27% critical
Good (≥70%)
Needs Attention
Critical (<40%)
No Response

## Slide 8
CYCLE INTELLIGENCE — REPEAT vs FIRST-TIME CALLERS
What happens when the same household is called again?
Context: 170 of 45,863 calls (0.37%) were to beneficiaries also called in a previous cycle. Every single engagement metric improved for repeat callers — suggesting familiarity with the AI bot drives better data quality.
Metric
First-time caller
Repeat caller
Change
Sample size
45,693 calls
170 calls
—
Consent rate
27.4%
44.7%
+63%
Q1 answered (usable)
20.0%
37.1%
+86%
Avg call duration
60 seconds
82 seconds
+37%
Full survey completed
3.4%
5.9%
~2×
BSI score /1.0
0.41
0.45
+9%
Quality satisfied
72.2%
89.3%
+17pp
Overall satisfied
51.8%
44.8%*
−7pp
* Repeat callers give more candid feedback — lower overall satisfaction may reflect more honest reporting, not worse service.
Recommendation: Prioritise re-calling the same households in Phase 2 — familiarity with the bot consistently improves data quality.

## Slide 9
ENERGY CONSUMPTION MONITORING MODEL
Theoretical daily kWh vs Real-time actual kWh | Per IMIS scheme
Formula: Theoretical kWh = (HH × 55 L × Head × 9.81) ÷ (Pump efficiency × Motor efficiency × 3,600,000)
Gap within 10% → 🟢 Green — Running well
Gap > 20% → 🟡 Amber Alert
Gap > 50% → 🔴 Red — Leakage / Theft / Failure
SCHEME INPUTS
Fixed parameters from IMIS portal
Pump Capacity (HP/kW)
The engine — determines max energy draw
Households Served
Drives demand: HH × 55 litres/person/day
Pipeline & Head (m)
Elevation + friction — higher head = more energy
IMIS Scheme ID
Links inputs to sensor data per scheme
ENERGY CALCULATION
Theoretical daily kWh formula engine
Volume Needed
HH × 55 L = total daily litres required
Pump Run Time
Volume ÷ flow rate = hours needed
55 LPCD Standard
JJM norm: 55 litres per capita per day
Theoretical kWh
HP × run hrs × 0.746 = expected energy
REAL-TIME DATA
Live sensor readings vs expected
Smart Energy Meter
Actual kWh/day — ground truth of consumption
IoT / SCADA Sensor
Pump run hours — was the pump over-running?
Flow Meter
Litres actually pumped — was 55 LPCD met?
Timestamp
Time-of-operation for scheduling analysis
ENERGY GAP
Actual kWh − Theoretical kWh
Positive = more energy than expected
EFFICIENCY %
(Theoretical ÷ Actual) × 100
<80% wasteful · >90% well-run
ALERT FLAG
Auto: Green / Amber / Red
Red = leakage, theft, or equipment failure
⚠ DATA GAPS: Pump HP/kW · Pipeline head (m) · Pump run hours · Flow meter (litres pumped) · Smart meter (actual kWh/day) — All required to activate this model

## Slide 10
SCHEME ENERGY DASHBOARD — DAILY MONITORING VIEW
IMIS ID: 30010486 | Scheme: Chandrapur MPWSS | District: Baksa, BTAD | Date: 04 Apr 2026
Theoretical kWh
18.4 kWh
Expected at 55 LPCD
Actual kWh
27.1 kWh
Smart meter today
Energy Gap
+8.7 kWh
Amber Alert
Efficiency
67.9%
Below 80% target
Litres Pumped
31,500 L
78.6% of 55 LPCD
Theoretical Energy — Step by Step
Households
44 HH
×
Daily standard
55 L/person
=
Total volume
2,420 L
÷
Pump flow rate
18 L/min
=
Run time
2.24 hrs
×
Pump power (HP×0.746)
7.46 kW
=
Theoretical kWh
16.7 kWh
* Uses example values — replace with actual IMIS scheme data
Gap Analysis & Alert Logic
Theoretical
18.4 kWh
Actual
27.1 kWh
+8.7
🟡 AMBER ALERT — Gap = +47.3% · Efficiency = 67.9%
Gap > 20% threshold. Possible: pump over-running, minor leakage, meter calibration.
Variables needed per scheme:
From IMIS (available): HH served, scheme name, district, zone
Missing (IMIS): Pump HP/kW, pipeline head in metres
IoT sensors needed: Actual kWh/day, pump run hours, litres pumped